## Slide 1
Sensing Plant and Soil Temperatures in Snowy Alpine Environments: Part II
Martha Apple1, James Gallagher2, Kevin Negus3, Jamison Ehlers3
1Biological Sciences, 3Electrical Engineering, Montana Technological University, 2OPeNDAP, Inc.

## Slide 2
Plant functional traits vary with position on periglacial patterned ground and near snowfields in the alpine tundra.
Periglacial patterned ground provides a mosaic of microhabitats.
Environmental sensing links plant functional traits with environmental signals.
FLIR (Forward Looking Infrared) images detect temperatures of plants and of patterned ground and snowfields.
We installed an array of soil temperature sensors but can only retrieve data at the sites.
Our alpine tundra sites are in the wilderness, have harsh winters, and are accessible only in late summer.
Research could be scaled up with wilderness-ready soil moisture sensors and with remote and year-round access to data.
We are developing a sensor system to send soil data to the internet via Iridium satellites.
Alpine Plant Ecology and Environmental Sensing

## Slide 3
At Goat Flat, Pintler Mountains, SW Montana, 2845 m, 46°02’47.03” N, 113°16’41.68”W, we:
Surveyed the distribution of plant species and functional traits
Installed 36 ONSET Hobo TidbitV2 #UTBI-001 Temperature Sensors at 4 sites, 5-10 cm in soil,
(18 sensors in center of polygons or brown stripes, 18 on edge of polygons or green stripes)
Green Edges of Polygons: Herbaceous plants, dwarf shrubs, + coniferous trees
Dryas octopetala, Salix arctica, Phyllodoce empetriformis,
Brown Centers of Polygons: Rhizomes, taproots, + herbaceous plants
Astragalus sp., Carex, Sedum lanceolatum, Gentiana calycosa

## Slide 4
Center of Polygon
Edge of Polygon

## Slide 5
MEASUREMENTS (°C)
Spot 1 58.2
Spot 2 53.3
Spot 3 41.6
Spot 4 35.1
Spot 5 32.5
Spot 6 29.8
Spot 7 27.7
Circle 1
Max. 29.4 Min. 27.3 Avg. 28.1
Circle 2 Max. 42.0 Min. 28.6 Avg. 38.2

## Slide 6
Tussocks at the
GLORIA Alpine site
on Mt. Pisa
in New Zealand
are cooler
than the surrounding
plants and ground.
Pacific Ocean
Beach Sand

## Slide 7
With the ESIP lab program:
We are developing prototype soil moisture sensors for year-round use on the alpine tundra
Sensors will be underground and not susceptible to wind and animal damage
Sensor data should be remotely accessible throughout the year
Data will be gathered from ~10 locations at the study site
Data will be sent to a data store accessible via the Internet.

## Slide 8: Current sensor design
Hardware simplification – Use RocketScream boards for all nodes
  Integrated real time clock, faster processor, more memory, LoRa, battery power features and low power modes
  Simpler than discrete components – decrease development time
Build significant local storage into node
  Using ruggedized SD memory cards; vast storage potential
Adopt a mesh network architecture
  Each leaf node will send its own information, listen/store from nearby nodes and selectively re-broadcast information from nearby nodes
  More robust than a star architecture
See poster: High Altitude Soil Testing: Increasing Accessibility of Data from Remote Locations, Jamison Ehlers; Martha Apple; Kevin Negus

## Slide 9: Experiments with LoRa
Tests run using moderate settings
  Bandwidth (BW) = 'Chips' per symbol
  Coding rate (CR) = Extra information sent for error correction
  Spreading factor (SF) = Number of chips used for each bit (Rc = Rb * 2SF)
Our tests:
  BW = 125kHz, CR =1, SF = 7
  Transmission power = 13 dBm
Message length 57 bytes (93 bytes in transmission frame)
Time on air: 107.78 ms

## Slide 10: Field Experiments with LoRa
Nodes separated from receiver by ~200 and ~300 ft
Used BW = 125 kHz, CR = 1, SF = 7
Transmission power = 13 dBm
Signal strength
  Line of sight: -95 to -120 dBm
  Ground Obstacle: -102 to -120 dBm
Line of sight
Ground obstacle

## Slide 11: LoRa Channel Activity Detection
Adding Channel Activity Detection reduced collisions from unsynchronized nodes
  #1 - Nodes started at the same time - Transmissions collide
  #2 - CAD added - one node waits for the other to complete transmission
It's not perfect...
  #3 - CAD may fail
Tests indicate it provides a benefit
3
2
1

## Slide 12
We acknowledge SURF (Summer Undergraduate Research Fellowship) and the ESIP Lab Program.